## Slide 1: Step-by-Step Example: Notional ASW Aircraft
Mission Profile
Mission Requirements
Loiter for three hours at 1500 nm from takeoff point, then return to base after another 20 min. loiter
Cruise Mach number: 0.6
Mission Equipment weight: 10,000 lbs.
Four-man crew totaling 800 lbs.
is known: 10,000 lbs + 800 lbs = 10,800 lbs

## Slide 2: Step-by-Step Example: Fuel Fraction, ,Estimation
Mission Fuel Fraction (MFF)
ASSUMPTION: weight change due to fuel consumption only

## Slide 3: Fuel Fraction Estimation by Mission Segments
For Cruise (Segment 3 & 5)
Endurance (Loiter) (Segments 4 & 6)
Other mission segments, use following estimates of Wi+1/Wi
Warmup and takeoff 0.97
Climb 0.985
Descent (consider part of Cruise) 1.0
Landing 0.995
Warmup and takeoff: W2 / W1 = 0.97
Climb: W3 / W2 = 0.985
For the ASW concept
Cruise (Segment 3): W4 / W3 = e{ – R*sfc/V(L/D)}

## Slide 4: Cruise Segment
Cruise (Segment 3): W4 / W3 = e{ – R*sfc/V(L/D)}
Given: R = 1500 nm = 9,114,000 ft
M = 0.6
Assume: Typical cruise altitude = 30,000 ft.
Estimate: Speed of sound = 994.8 ft/s
V = 596.9 ft/s
Assume: High bypass ratio turbofans for efficiency
Estimate: sfc = 0.5 lb/hr/lb = 0.000139 lb/s/lb
Assume: AR = 7 (Combined Wing and Canard)
Estimate: Swet/Sref =5.5
Wetted Aspect Ratio = 7/ (5.5) = 1.27
L/Dmax = 16
Assume: Cruise L/D = 0.866 (L/D)max
Estimate: L/D = 13.9
Cruise (Segment 3) fuel fraction: W4 / W3 = 0.8584
Cruise (Segment 5) fuel fraction:
W6 / W5 = e{ – R*sfc/V(L/D)}
W6 / W5 = 0.8584

## Slide 5: Loiter and Land Segments
Loiter (Segment 4): W5 / W4 = e{ – E*sfc/(L/D)}
Given: E = 3 hrs = 10,800 sec
Estimate: sfc = 0.4 lb/hr/lb = 0.000111 lb/s/lb
L/D = L/Dmax = 16
W5 / W4 = 0.9278
Loiter (Segment 6): W7 / W6 = e{ – E*sfc/(L/D)}
Given: E = 20 min = 1,200 sec W7 / W6 = 0.9917
Landing (Segment 7): W8 / W7 = 0.995
Therefore W8 / W1 = 0.6444 from
Mission Fuel Fraction = (1 – W8 / W1 )
Fuel [Weight] Fraction: Wfuel / WTO = (1 + 0.05 + 0.01) (1 – 0.6441)
= 0.3768

## Slide 6: TOGW Iterations
lbs
Compute empty weight fraction:
Compute mission fuel:
Mission Profile
Aerodynamic Characteristics
Propulsive Characteristics
Compute new TOGW
Initialize by guessing
Stop when converged
TOGW | W-fixed | Fuel fraction | Weight fraction | Empty weight | TOGW | Difference
50000 | 10800 | 0.3773 | 0.44 | 21803.44 | 57868 | 
57868 | 10800 | 0.3773 | 0.43 | 24977.66 | 56524 | -1344
56524 | 10800 | 0.3773 | 0.43 | 24437.64 | 56735 | 211
56735 | 10800 | 0.3773 | 0.43 | 24522.47 | 56701 | -34
56701 | 10800 | 0.3773 | 0.43 | 24508.97 | 56707 | 5
56707 | 10800 | 0.3773 | 0.43 | 24511.12 | 56706 | -1
Is it a reasonable estimate?

## Slide 7: Sanity Check
WTO = 52,539 lbs.
We are in the “right ballpark”